## Slide 1: Week 5b
COMPUTATIONAL MATHEMATICS

## Slide 2: Reference
Kisualaas, Jann. (2013). Numerical Methods in Engineering with Python 3. Cambridge University Press.
Johansson, Robert. (2015). Chapter 5. Equation Solving. Numerical Python: A Practical Techniques Approach for Industry, Apress.
Chapra, S. C., and Raymond P. Canale. (2010). Numerical methods for engineers, Sixth edition, McGraw Hill.
Kaw, A. (n.d.). Numerical Methods. Retrieved March 20, 2020, from https://nm.mathforcollege.com/

## Slide 3: Two sources of numerical error
Round off error
Truncation error

## Slide 4: Round off Error
Caused by representing a number approximately

## Slide 5: Problems created by round off error
28 Americans were killed on February 25, 1991 by an Iraqi Scud missile in Dhahran, Saudi Arabia.
The patriot defense system failed to track and intercept the Scud. Why?

## Slide 6: Problem with Patriot missile
Clock cycle of 1/10 seconds was represented in 24-bit fixed point register created an error of 9.5 x 10-8 seconds.
The battery was on for 100 consecutive hours, thus causing an inaccuracy of

## Slide 7: Problem (cont.)
The shift calculated in the ranging system of the missile was 687 meters.
The target was considered to be out of range at a distance greater than 137 meters.

## Slide 8: Effect of Carrying Significant Digits in Calculations

## Slide 9: Find the contraction in the diameter
Ta=80oF; Tc=-108oF; D=12.363”
α = a0+ a1T + a2T2

## Slide 10: Thermal Expansion Coefficient vs Temperature
T(oF) | α (μin/in/oF)
-340 | 2.45
-300 | 3.07
-220 | 4.08
-160 | 4.72
-80 | 5.43
0 | 6.00
40 | 6.24
80 | 6.47

## Slide 11: Regressing Data in Excel (general format)
α = -1E-05T2 + 0.0062T + 6.0234

## Slide 12: Observed and Predicted Values
T(oF) | α (μin/in/oF) Given | α (μin/in/oF) Predicted
-340 | 2.45 | 2.76
-300 | 3.07 | 3.26
-220 | 4.08 | 4.18
-160 | 4.72 | 4.78
-80 | 5.43 | 5.46
0 | 6.00 | 6.02
40 | 6.24 | 6.26
80 | 6.47 | 6.46
α = -1E-05T2 + 0.0062T + 6.0234

## Slide 13: Regressing Data in Excel (scientific format)
α = -1.2360E-05T2 + 6.2714E-03T + 6.0234

## Slide 14: Observed and Predicted Values
T(oF) | α (μin/in/oF) Given | α (μin/in/oF) Predicted
-340 | 2.45 | 2.46
-300 | 3.07 | 3.03
-220 | 4.08 | 4.05
-160 | 4.72 | 4.70
-80 | 5.43 | 5.44
0 | 6.00 | 6.02
40 | 6.24 | 6.25
80 | 6.47 | 6.45
α = -1.2360E-05T2 + 6.2714E-03T + 6.0234

## Slide 15: Observed and Predicted Values
T(oF) | α (μin/in/oF) Given | α (μin/in/oF) Predicted | α (μin/in/oF) Predicted
-340 | 2.45 | 2.46 | 2.76
-300 | 3.07 | 3.03 | 3.26
-220 | 4.08 | 4.05 | 4.18
-160 | 4.72 | 4.70 | 4.78
-80 | 5.43 | 5.44 | 5.46
0 | 6.00 | 6.02 | 6.02
40 | 6.24 | 6.25 | 6.26
80 | 6.47 | 6.45 | 6.46
α = -1.2360E-05T2 + 6.2714E-03T + 6.0234
α = -1E-05T2 + 0.0062T + 6.0234

## Slide 16: Truncation error
Error caused by truncating or approximating a mathematical procedure.

## Slide 17: Example of Truncation Error
Taking only a few terms of a Maclaurin series to
approximate
If only 3 terms are used,

## Slide 18: Another Example of Truncation Error
Using a finite
to approximate
P
Q
secant line
tangent line
Figure 1. Approximate derivative using finite Δx

## Slide 19: Another Example of Truncation Error
Using finite rectangles to approximate an integral.

## Slide 20: Example 1 —Maclaurin series
Calculate the value of
with an absolute
relative approximate error of less than 1%.
n |  |  | 
1 | 1 | __ | ___
2 | 2.2 | 1.2 | 54.545
3 | 2.92 | 0.72 | 24.658
4 | 3.208 | 0.288 | 8.9776
5 | 3.2944 | 0.0864 | 2.6226
6 | 3.3151 | 0.020736 | 0.62550
6 terms are required. How many are required to get at least 1 significant digit correct in your answer?

## Slide 21: Example 2 —Differentiation
Find
for
using
and
The actual value is
Truncation error is then,
Can you find the truncation error with

## Slide 22: Example 3 — Integration
Use two rectangles of equal width to approximate the area under the curve for
over the interval

## Slide 23: Integration example (cont.)
Choosing a width of 3, we have
Actual value is given by
Truncation error is then
Can you find the truncation error with 4 rectangles?